## Slide 1: TRAINING MANUAL FOR HANDYMEN

## Slide 2
MODULE 1:
Defining Day-today maintenance
MODULE 2 :
Maintenance guidelines for schools (daily, weekly, monthly and annually)
MODULE 3 :
Identification of immediate safety risks
MODULE 4:
Guidelines for responding to an infrastructure-related emergency
MODULE 5:
Process for logging an emergency maintenance request
MODULE 6:
The assessment of potential structural defects
MODULE 7:
Identification of different Mobiles

## Slide 3
What is maintenance?
Keeping a facility in good working condition so that it can function properly, restoring it to its original condition, carrying out repairs and replacing faulty or broken parts.
Why do we carry out maintenance work?
To save money and allowing facilities to be used for many years.
To keep facilities in good condition and ensuring positive influence in attendance and achievement levels of educators and learners.
To reduce the risk by preventing failures and damages of facilities and even loss of life.
DAY-TO-DAY MAINTENANCE

## Slide 4
PLANNED MAINTENANCE
Planned maintenance is organized according to plan and is made up of:
Statutory maintenance
This form of maintenance can apply to both preventative and condition based maintenance where legislation, regulations, standards and codes of practice may require specific forms of maintenance to be carried out to provide what in their respective fields are regarded as the minimum form of maintenance required. E.g. inspection and servicing of fire extinguishers and hose reels.
II. Preventative maintenance
This form comprises actions performed to retain an asset in its required condition or standard, and sets out to prevent failure by providing systematic inspection and monitoring to detect and prevent deterioration and / or failure, and includes testing to confirm correct operation. E.g. service the facility every year to prevent future failure even if it’s still in a good condition.
III. Condition based maintenance
This form of maintenance is to restore an asset to its required condition. The work could be programmed in terms of condition assessments or alternatively conducted as random additions to the program based on a prioritized process or system. E.g. repair a leaking tap, if it’s in a good condition, then no maintenance is done.

## Slide 5
MAINTENANCE GUIDELINES FOR SCHOOLS (Daily and Weekly)
The following is a list of simple daily and weekly maintenance to keep buildings in good condition:
sweep and wash the floor and verandas daily
clean and wash down toilets every day
clean windows every week
clean storm-drains around the buildings every week especially during rainy season
collect rubbish every day and burn the rubbish daily or weekly depending upon the amount and bury the ash.
cut the grass every week especially during rainy season

## Slide 6
CHECKLIST FOR DAILY AND WEEKLY MAINTENANCE
MAINTENANCE ITEM | WEEK | RESPONSIBILITY | ACTION TAKEN
SWEEP AND WASH THE FLOOR AND VERANDAS |  |  | 
CLEAN AND WASH DOWN TOILETS |  |  | 
CLEAN WINDOWS |  |  | 
CLEAN STORM-DRAINS |  |  | 
COLLECT RUBBISH |  |  | 
CUT THE GRASS |  |  | 

## Slide 7
MAINTENANCE GUIDELINES FOR SCHOOLS (Monthly and annually)
Every month, a more detailed inspection should be made of the school buildings and grounds. The list below gives a simple building monthly maintenance check internally and externally and on grounds:
Trim any trees or shrubs close to the buildings
Check that septic tanks (where applicable) are not full
Check main water pipes and taps for leaks and repair as necessary
Check roofs finished with corrugated steel or fiber-cement sheets for loose nails of screws and tighten, seal or replace as necessary
Check the external light fittings and switches if they are working, switch covers are properly fixed and not damaged; clean light fittings as necessary
Check ceilings for damp patches that indicate roof leaks
Check that doors are closing properly and not touching the floor, check that door handles and striking plate are fixed and that keys have not been lost. Oil hinges, handles and locks and adjust locking plates and bolts as necessary

## Slide 8
CHECKLIST FOR DAILY AND WEEKLY MAINTENANCE
MAINTENANCE ITEM | RESPONSIBILITY | PROBLEM | ACTION TAKEN
Trim any trees or shrubs |  |  | 
Check that septic tanks are not full |  |  | 
Check main water pipes and taps for leaks |  |  | 
Check the external light fittings and switches |  |  | 
Check ceilings for damp patches |  |  | 
Check doors are closing properly, check that door handles and striking plate are fixed and that keys have not been lost. |  |  | 

## Slide 9
MAINTENANCE GUIDELINES FOR SCHOOLS (annually)
Every year, the school grounds and buildings should be thoroughly inspected. The list below gives a simple annual buildings maintenance check internally and externally and on the grounds:
Check paving around buildings
check paths and roads within the site. check for any surface cracks or damage and repair as necessary
check walls or fences and gates for damage and repair or replace as necessary
check external electrical installations
Mobile classrooms: check steel cladding for rust and loose fixings and replace or tighten as necessary
check that toilets are operating properly and are not blocked. if cisterns are fitted, check flushing mechanisms, check all pipe leaks replace and repair as necessary

## Slide 10
ANNUAL MAINTENANCE CHECKS
MAINTENANCE ITEM | RESPONSIBILITY | PROBLEM | ACTION TAKEN
Check paving around buildings |  |  | 
Check paths and roads within the site |  |  | 
Check walls or fences and gates |  |  | 
Check external electrical installations |  |  | 
Check steel cladding for rust and loose fixings |  |  | 
Check that toilets are operating properly and are not blocked |  |  | 

## Slide 11
IDENTIFICATION OF IMMEDIATE SAFETY RISKS
A school risk assessment is a systematic inspection that identifies and controls immediate safety risks (hazards) within the school premises.
Beyond complying with legislative requirements, school risk assessments are conducted by school management teams to ensure a healthy and safe environment for leaners, teachers, administrators and other staff.
School risk assessments are conducted regularly to identify the likelihood of injury to a person after being exposed to hazard and examines whether existing control measures are sufficient.

## Slide 12
IDENTIFICATION OF IMMEDIATE SAFETY RISKS (Continued)
A basic school risk assessment generally asks the following key questions:
What are the immediate risks identified ?
Who might be harmed?
How they might be harmed?
What are the existing precautions? Is it enough to control the hazard?
What further actions are needed to eliminate the immediate risk?
These questions make it easy to evaluate the school’s immediate risks

## Slide 13
SCHOOL RISK ASSESSMENT TEMPLATE
Question | Response | Details
Assessment |  | 
Hazards? |  | 
Identify the hazard |  | 
Who might be harmed? |  | 
How they might be harmed (i.e. what type of injury or health issues might occur)? |  | 
photo of Hazard |  | 
Risk rating |  | 

## Slide 14
GUIDELINES FOR RESPONDING TO AN INFRASTRUCTURE-RELATED EMERGENCY
Establish the Context
Define the problem and establish a risk management framework that includes the nature and scope of the problem and what process will be undertaken
Identify, Analyze and Evaluate risks
Identify and describe the source of the infrastructure-related emergency.
Analyze the risk associated with the problem by determining the consequences of the identified risks.
Compare risk against risk evaluation criteria.
Prioritize the risk and decide on risk acceptability

## Slide 15
Treat Risks
Identify and evaluate treatments.
Respond to the level of risk by deciding which source of risk can be addressed immediately and which stakeholders, communities or environmental factors can be addressed to reduce risk.
Note or model changes to obtain the new level of risk.
Select treatments, plan and implement on a continuous basis
Monitor and Review
Systems that monitor and review risk, and its management, must be established and maintained.
Latent and residual risk are ever-present.
Emergency response management must be on-going to ensure that change and uncertainty can be accommodated.

## Slide 16
PROCESS FOR LOGGING AND EMERGENCY MAINTENANCE REQUEST
Emergency maintenance is undertaken to prevent infrastructure related emergencies that could lead to either loss of life, health deterioration, or interference with the learning process
Inspection
Carry out an inspection
Identify the risk and describe the source of risk
Picture Evidence
Take pictures as evidence of the risk and need for emergency maintenance
Consultation
Consult school management about logging an emergency maintenance request
Emergency Maintenance Request
School Principal should then send a formal request to the Infrastructure Directorate stating the need for emergency maintenance
The request should also include pictures taken during inspection

## Slide 17
ASSESSMENT OF POTENTIAL STRUCTURAL DEFECTS
Structural defects can be caused by a number of things.
Initially, defects may appear as a minor crack in the wall and termites which might be found on the walls, but in the long term defects can lead to the collapse of the entire wall.
In order to address the cracks, possible causes have to be detected, causes like movement or settlement of the structure overtime, roots of trees embedded beneath the structure and uncontrolled slopes/failure to build, proper stormwater drainage which makes it easy for rain water to penetrate the structure.
Once the potential cause has been detected, it is then that the possible solution is attained to decide as to whether the structure is to be demolished then rebuilt again or the cracks are sealed.
In the case of termites, pest control is ordinarily the solution

## Slide 18
IDENTIFICATION OF DIFFERENT MOBILES
GRADE R
Prefabricated mobile double Grade R classroom building and including refurbishment of interior with required equipment and furniture. Size 18m x 7m = ±126m2 with verandah size: 18m x 1.5m at ±27m2. The interior of the building will also be provided with a store area of size 3m x 3m = ±9m2 and ablution area of size 4m x 3m = ±12m2 and overall a standard ceiling height of no less than 2400mm. (Accordingly attached layout and specification. Overall sizes may vary with ±200mm tolerance).
KITCHEN UNIT
Prefabricated mobile kitchen unit with a minimum floor area of ±21.08m2 per kitchen ±6.2m x 3.4m with verandah size: 6.2m x 1.8m at ±11.16m2. The interior of the building must also be provided with a store room of Size 3.4m x 1.4m = ±4.76m2 and overall a standard ceiling height of no less than 2700mm. (Accordingly attached layout and specification. Overall sizes may vary with ±200mm tolerance).
CLASSROOM
Mobile classrooms must be detachable in maximum two sections and with a minimum floor area of 49m2 per unit and a standard ceiling height of not less than 2600mm. (Accordingly attached Layout. Overall sizes may vary with ±200mm tolerance).
ADMINISTRATION BLOCK
The Mobile administration block must be detachable in maximum two sections and with a minimum floor area of 126m2 overall and a standard ceiling height of not less than 2600mm. (Accordingly attached layout and sizes may vary with ±200mm tolerance).
ABLUTION
The Mobile ablution block one for for girls and for boys with a minimum floor area of 27m2. The standard ceiling height may not be less than 2600mm. (Accordingly attached layout. Overall sizes may vary with ±200mm tolerance).

## Slide 19
19